## Slide 1
D-SI 2.2.0 Beta
Overview extension
2023-08-30

## Slide 2
Thanks to all colleagues and partners who have proposed many valuable ideas for improvements and additions to the D-SI in the past months.
You helped the D-SI to make a major step into the future increasing its quality and useability for a wider range of (metrological) applications.

## Slide 3: D-SI
D-SI
Metadata Modell
Implementation Metadata Modell
Instances of data with D-SI elements
<si:real>
<si:label>length</si:label>
<si:value>1.34</si:value>
<si:unit>\metre</si:unit>
<si:dateTime>
2021-10-28T17:00:00.00+02:00
</si:dateTime>
</si:real>
Broschure
DOI: 10.5281/zenodo.3816686
Machine-2-machine exchange
universal
unambiguous
save
Easy-to-understand
XML Schema
(JSON Schema)
(Ontology OWL2)
XML element, e.g., in Digital Calibration Certificate
JSON, HDF5, CSV,…
Repository
https://gitlab1.ptb.de/d-ptb/d-si/xsd-d-si
Notes: A very small set of variants supporting the necessary functions
Redundancy avoided where possible
Fostering direct use of data without need for conversion

## Slide 4: D-SI timeline
2018 2019 2020 2021 2022 2023 2024
EMPIR SmartCom start of D-SI
D-SI initial release metadata model and XML implementation (version 1.x.x)
D-SI update for SI redefinition
D-SI extension XML implementation (version 2.x.x)
Long Term Stable Version
Larger extension
D-SI model and XML implementation (version 2.2.0) following user feedback
Development of services advancing semantic interoperability of D-SI data (e.g., link to BIPM’s SI Reference Point)
D-SI entering applications
FAIR & Level 4 Maturity
(semantics, machine-actionable)

## Slide 5: Motivation
Addressing DCC user needs around the world
Implementing feedback from DKD groups
Addressing requirements from communities beyond calibration
Update since last changes were implemented 2021
Beta version 2.2.0 2023 drafting updates and extensions
Now pilot phase for testing, etc. before official release

## Slide 6: Extensions
Type of quantity
Standard measurement uncertainty
Element names for uncertainty
Disambiguating uncertainty statements
Voids (NaN, undefined values)
Significant Digit
Complex as XML list
Additional components in units
Preparing semantics for future
Sanitizing XSD

## Slide 7: Overview
1. Type of quantity

## Slide 8: si:quantityType
Information on underlying quantity is essential to achieve ISO Smart level 4 of machine interoperable data
Important: Identifiers for basic physical quantities (length, mass, ratios,…) not measurands (radius of circle, voltage at input, …)
Thus, introduction of quantity kind (type) using PIDs from QUDT.org ontology
Implementation considering extensions in the future such as using additional vocabularies from ISO, IEC etc.
Notes: Der XML Datentyp stellt URL Bereit mit der Metadaten zu Größe bei QUDT abgerufen warden können
XML Umsetzung ist so konzipert, dass später auch andere Bezeichner, zum Beispiel von ISO eingesetzt warden könnten.

## Slide 9: si:quantityType - implementation
Extensible XSD
<xs:element name="quantityType" type="xs:string" abstract="true"/>
<xs:element name="quantityTypeQUDT" substitutionGroup="si:quantityType" type="qudt:quantityKind"/>
<xs:element name="quantityTypeIEC" substitutionGroup="si:quantityType"/>
<xs:element name="real">
...
<xs:element ref="si:quantityType" minOccurs="0"/> …
Allowing
<si:real>
…
<si:quantityTypeQUDT>Length</si:quantityTypeQUDT> …
</si:real>
PID: https://qudt.org/vocab/quantitykind/Length(.ttl)
Notes: Der XML Datentyp stellt URL Bereit mit der Metadaten zu Größe bei QUDT abgerufen warden können
XML Umsetzung ist so konzipert, dass später auch andere Bezeichner, zum Beispiel von ISO eingesetzt warden könnten.

## Slide 10: Overview
2. Standard measurement uncertainty

## Slide 11: Standard measurement uncertainty
Introducing element to provide minimum (initial) information on standard measurement uncertainty
<si:standardMU>
<si:valueStandardMU>0.05</si:valueStandardMU> (mandatory)
<si:distribution>normal</si:distribution> (optional)
</si:standardMU>

## Slide 12: Overview
3. Element names for uncertainty

## Slide 13: Element names for uncertainties
Need
Improvement of naming for users and applications discussed with DKD FA Measurement Uncertainty (lead Dr. Koch)
Improvement of underlying types for future semantics
Realization
Extension of D-SI with uncertainty elements using improved (new) naming
Preservation of old uncertainty element names to guarantee backwards compatibility (deprecated elements)

## Slide 14: Example: expanded uncertainty
<si:real>
<si:value>1.00</si:value>
<si:unit>\metre</si:unit>
<si:measurementUncertaintyUnivariate>
<si:expandedMU>
<si:valueExpandedMU>0.10</si:valueExpandedMU>
<si:coverageFactor>1.96</si:coverageFactor>
<si:coverageProbability>0.95</si:coverageProbability>
<si:distribution>normal</si:distribution>
</si:expandedMU>
</si:measurementUncertaintyUnivariate>
</si:real>
<si:real>
<si:value>1.00</si:value>
<si:unit>\metre</si:unit>
<si:expandedUnc>
<si:uncertainty>0.10</si:uncertainty>
<si:coverageFactor>1.96</si:coverageFactor>
<si:coverageProbability>0.95</si:coverageProbability>
<si:distribution>normal</si:distribution>
</si:expandedUnc>
</si:real>
becomes
New:
Top level element si:measurementUncertaintyUnivariate
Individual MU value element

## Slide 15: Change of element names and types
New tag | Old tag | New type | Old type
si:expandedMU | si:expandedUnc | si:expandedMUType | si:expandedUncType
si:coverageIntervalMU | si:coverageInterval | si:coverageIntervalMUType | si:coverageIntervalType
si:standardMU | - | si:standardMUType | -
si:valueExpandedMU | si:uncertainty | si:valueExpandedMUType | si:uncertaintyValueType
si:valueStandardMU | si:standardUnc | si:valueStandardMUType | si:uncertaintyValueType
si:intervalMin | si:intervalMin | si:intervalMinType | si:decimalType
si:intervalMax | si:intervalMax | si:intervalMaxType | si:decimalType

## Slide 16: Overview
4. Disambiguating uncertainty statements

## Slide 17: Refinement of documentation
consistent: k=1.96, p=0.95, normal distribution
inconsisten: k=2.00, p=0.95, normal distribution
Consistency of data responsibility of data creator
Use k-value and distribution information if p-value is inconsistent
k=2.00, normal distribution  p > 0.95
k-value statement
What are the values that should be used at subsequent calculations?
Statement of distribution
Recommendation to always provide information on distribution
If si:distribution not provided, then distribution unknown (not default „normal distribution“

## Slide 18: Overview
5. Voids (NaN, undefined values)

## Slide 19: Voids - basics
“NaN” in xs:double
Useable in XML, JSON, …
documentation in D-SI as missing value. Definition of reason for missing value not part of D-SI.
Medal “BRONZE”
… in real, complex, all lists, and uncertainty statements
Background:
Need in pharma (ALCOA+ principles) and several applications vs.
D-SI: high risk of ambiguous statements if improperly introduced
solution

## Slide 20: Voids – in uncertainty statements
Voids supported in uncertainty statements
allowed
<si:uncertainty>NaN</si:uncertainty>
<si:coverageFactor>NaN</si:coverageFactor>
<si:coverageProbability>NaN</si:coverageProbability>
forbidden
<si:uncertainty>NaN</si:uncertainty>
<si:coverageFactor>1.96</si:coverageFactor>
<si:coverageProbability>0.95</si:coverageProbability>

## Slide 21: Overview
6. Significant Digit

## Slide 22: Significant Digit - Standardization
03.0560 mm
display value
recorded value
3.06 mm
3 significant digits
(DKD L-13)
significant digit 10-2
(ISO/IEC2382:2015en)
quantisation
00.0000 mm
?
3.05 mm
03.0560 mm
00.0000 mm
Rounding range value
(ISO/IEC 80000-1)
0.01 mm
0.01 mm
0.0001 mm
0.0001 mm
0.00 mm
si:significantDigit
-2

## Slide 23: Significant Digit – D-SI implementation
<si:real>
<si:value>3.06</si:value>
<si:unit>\metre</si:unit>
<si:significantDigit>-2</si:significantDigit>
</si:real>
<xs:simpleType name="significantDigitType">
<xs:annotation>
<xs:documentation xml:lang="en">
Type providing number of significant digitis
with separation by blank spaces.
</xs:documentation>
</xs:annotation>
<xs:restriction base="xs:integer"/> </xs:simpleType>
write
read
Software
3.06  03.0560 (consider rounding in U)
3.05999999  3.06
New: optional element si:significantDigit

## Slide 24: Significant Digit - Remarks
Recommendation by D-SI to encode influences from significant digits and rounding as component contributing to the value of the measurement uncertainty for unambiguous use of data in digital systems.
Provision of the significant digit is optional and can be applied by users, who are required to provide it. The D-SI solution is compliant to ISO/IEC 80000-1, ISO/IEC2382:2015en, and calibration guideline requirements.
Provision of more metadata, e.g., rounding methods etc. is subject to higher level data structures such as calibration metadata, etc.

## Slide 25: Overview
7. Complex as XML list

## Slide 26: Complex as XML List
Concept the same as XML list for real & improved names of uncertainty elements
<si:complexListXMLList>
<si:valueRealXMLList>1 2 3</si:valueRealXMLList>
<si:valueImagXMLList>4 5 6</si:valueImagXMLList>
<si:unitXMLList>\metre \second \kilogram</si:unitXMLList>
<si:measurementUncertaintyBivariateXMLList>
<si:ellipsoidalRegionMUXMLList>
<si:covarianceMatrixXMLList>
<si:columnXMLList>
<si:covarianceXMLList>
<si:valueXMLList>0.3 0.4 0.5</si:valueRealXMLList>
<si:unitXMLList>\metre\metre</si:unitXMLList>
</si:covarianceXMLList>
...
</si:measurementUncertaintyBivariateXMLList>
</si:complexListXMLList>

## Slide 27: Overview
8. Additional components in units

## Slide 28: Units – additional units and components
Dimension one units
Needed, as allowed in 9th addition of SI brochure

## Slide 29: Units – additional units and components
New SI prefixes and binary prefixes

## Slide 30: Units – additional operator “\per”

## Slide 31: Overview
9. Preparing semantics for future

## Slide 32: Semantics
D-SI Metadata Model & Implementations
Common Data Model
Level 2-3
Semantic Data Model (semantic interoperability layer)
D-SI Element Types & URLs (PIDs)
BIPM SI Ref. Point
VIM, GUM vocab., ...
Level 3-4
FAIR
FAIR
D-SI extension enabling Semantic Data Model on top of Common Data Model
Interoperation with Knowledge Graphs, linked data, ontologies, …

## Slide 33: Semantics – What are the issues?
Each component (type) in the D-SI metadata model needs to allow a machine-actionable link to metadata providing its meaning (semantics).
However, the initial design did not have this need in mind and the definition and use of some types is too ambiguous to establish unambiguous semantic links, e.g.
si:label and si:distribution have different meaning but are of the same type xs:string.

## Slide 34: Semantics Example
becomes

## Slide 35: Semantics - improvements
All updates regarding quantity types and improved uncertainty elements establishing ability for unique semantic linking.
Unique element names and types whenever data has different meaning.
Specific simple types based on String and Double adding meaning like “min value type”, “label type”, “quantityTypeQUDT”, …
However, ensuring backwards compatibility of the D-SI leads to some limitation to the ability to disambiguate all types for better semantics.

## Slide 36: Overview
10. Sanitizing XSD

## Slide 37: Sanitizing XSD
Old structure New structure (easy to read)
<element1> <element1>
<element2> <element1Type>
… <element2>
<element1Type> <element2Type>
<element2Type> …
… <simpleType1>
<simpleType1> …
…

## Slide 38: Summary
Type of quantity
Standard measurement uncertainty
Element names for uncertainty
Disambiguating uncertainty statements
Voids (NaN, undefined values)
Significant Digit
Complex as XML list
Additional components in units
Preparing semantics for future
Sanitizing XSD

## Slide 39: Summary
April 2023 D-SI 2.2.0 beta draft
Since then piloting of D-SI 2.2.0 beta
  Documentation and communication of changes
  Collecting initial feedback from DCC users
  Fixing bugs
  Updating D-SI documentation
Planning steps and roadmap for release (aim is end of 2023)

## Slide 40
Daniel Hutzschenreuter
Physikalisch-Technische Bundesanstalt
Daniel.Hutzschenreuter@ptb.de
2023-07