## Slide 1
EMPIR CALL 2020
Metrology infrastructure for high-pressure gas and liquified hydrogen flows
CFD Workshop
Part 3: Tutorial case of a critical nozzle
"FROM Adjusting the mesh TO visualiZing the flow field"
Sebastian Weiss
Working Groups 8.41 “Modelling and Simulation” and 1.45 “Hydrogen Quantity Metering”
Physikalisch-Technische Bundesanstalt (PTB), Berlin, Germany
CFD Workshop – Part 3 15 June 2023 Borås, SWE

## Slide 2: Tutorial case description
Measured nozzle contour from project
Inlet:
Outlet:
Wall:
High-pressure hydrogen flow through a cylindrical non-ideal critical nozzle
A
A
A – A
Simulation is conducted with OpenFOAM version:
  ESI OpenCFD Release OpenFOAM® v2012 (20 12)

## Slide 3: Agenda (Part 1)
Geometry creation
Mesh creation
Numerical setup
  Boundary conditions
  Turbulence model
  Real gas model
  Numerical settings
/
/
/
turbulent thermal diffusivity
turbulence kinetic energy
turbulent viscosity
turbulence specific dissipation rate
pressure
temperature
velocity
thermophysical properties
turbulence properties
mesh settings
simulation settings
decomposition settings
mesh extrusion settings
numerical schemes
numerical solvers
nozzle contour file
OpenFOAM folder structure
Pre-processing

## Slide 4: Agenda (Part 1)
Geometry creation
Mesh creation
Numerical setup
  Boundary conditions
  Turbulence model
  Real gas model
  Numerical settings
/
/
/
turbulent thermal diffusivity
turbulence kinetic energy
turbulent viscosity
turbulence specific dissipation rate
pressure
temperature
velocity
thermophysical properties
turbulence properties
mesh settings
simulation settings
decomposition settings
mesh extrusion settings
numerical schemes
numerical solvers
nozzle contour file
OpenFOAM folder structure
Pre-processing

## Slide 5: 1. Geometry creation
Nozzle contour file is created using Python script
Specific file format required for later use in meshing tool
  BSz: vector of axial nozzle coordinates
  BSy: vector of radial nozzle coordinates
  BSd: index of throat diameter position
Note: throat diameter is always normalized to 1 in this file
Functions are available for:
  Toroidal nozzles (Tor_ideal)
  Cylindrical nozzles (Cyl_ideal)
  Measured nozzles (Meas_CFVN)
  Creation of geometry file (create_geometry_file)
Let’s have a look at how to create the geometry file Meas_Cyl.out for our tutorial case
Nozzle contour file
Meas_Cyl.out
Nozzle contour file format
(for use in blockMesh)

## Slide 6: 1. Geometry creation
Ideal toroidal nozzle:
Function: Tor_ideal(l, al, nz)
Parameters:
l nozzle length (in d)
al diffusor angle (in °)
nz number of points
Ideal cylindrical nozzle:
Function: Cyl_ideal(l, al, nz)
Parameters:
l nozzle length (in d)
al diffusor angle (in °)
nz number of points
Recap of the geometry functions
zd, yd, dpos = Tor_ideal(9.0, 4.0, 1000)
zd, yd, dpos = Cyl_ideal(9.0, 4.0, 1000)
l
al
nz

## Slide 7: 1. Geometry creation
Measured nozzle:
Function: Meas_CFVN(meas_data, NType, l, n_in, n_out)
Recap of the geometry functions
zd, yd, dpos, zdRaw, ydRaw = Meas_CFVN(‘Cyl_D1_meas.txt’, 0, 9.0, 40, 25)
Parameters:
meas_data file containing measured contour data
(list of z and y positions, tab-separated)
NType nozzle type (0 if cylindrical, 1 if toroidal)
l nozzle length (in d)
n_in point index for inlet circle (in meas_data)
n_out point index for outlet slope
(counted from last index in meas_data)
l
n_in
n_out
Cyl_D1_meas.txt
From CMM measurement:
meas_data
NType
0
1
Cyl.
Tor.
meas_data

## Slide 8: 1. Geometry creation
Creation of geometry file:
Function: create_geometry_file(name, BSz, Bsy, BSd)
Parameters:
name name of output file (here: Meas_Cyl.out)
BSz vector of axial nozzle coordinates (already created)
BSy vector of radial nozzle coordinates (already created)
BSd index of throat diameter position (already created)
Recap of the geometry functions
…
Output file (Meas_Cyl.out)
Geometry is created 
…

## Slide 9: Agenda (Part 1)
Geometry creation
Mesh creation
Numerical setup
  Boundary conditions
  Turbulence model
  Real gas model
  Numerical settings
/
/
/
turbulent thermal diffusivity
turbulence kinetic energy
turbulent viscosity
turbulence specific dissipation rate
pressure
temperature
velocity
thermophysical properties
turbulence properties
mesh settings
simulation settings
decomposition settings
mesh extrusion settings
numerical schemes
numerical solvers
nozzle contour file
OpenFOAM folder structure
Pre-processing

## Slide 10: 2. Mesh creation
Mesh is created using blockMesh utility in OpenFOAM
blockMesh generates hexaedral meshes from geometry using block structure
Mesh information is written in blockMeshDict file
We will create the mesh for the measured cylindrical nozzle geometry with a blockMesh-based nozzle meshing tool
But first, let’s have a look at a simple example to understand the blockMesh structure
Simple example

## Slide 11: 2. Mesh creation
blocks: Ordered list of vertex labels and mesh size
Vertex numbers
Cell expansion ratios
Number of cells in each direction
vertices: List of vertex coordinates
0
1
3
4
5
6
7
2
z
y
x
3 mm
0.1 mm
0.7 mm
scale: Scaling factor (0.001 scales to mm)
Simple example (blockMeshDict file)
0
1
3
4
5
6
7
2

## Slide 12: 2. Mesh creation
boundary: List of boundary faces and type
edges: Used to define arc or spline edges
0
1
3
4
5
6
7
2
inlet
outlet
axis
top
front
back

## Slide 13: 2. Mesh creation
extrudeMeshDict: Used to create a 5° wedge sector mesh
Now we create the mesh for our tutorial case using more advanced nozzle meshing tool
0
1
3
4
5
6
7
2
inlet
outlet
axis
top
front
back

## Slide 14: 2. Mesh creation
cy
li
Input variables
Geometry
sc scaling factor (sc = 0.001  d = 1 mm)
li inlet length (in d)
Nozzle contour file
Mesh
cy number of cells in the y-direction
cz number of cells in the z-direction
gy grading in the y-direction
Nozzle contour
Meas_Cyl.out
d/2
cz
t2
t1
gy = t2/t1
y
z
// * * * * * * * * * * * MESH GENERATION TOOL OF 2D NOZZLE * * * * * * * * * //
// //
// * * * * * * * * * * * * * * * INPUT PARAMETERS * * * * * * * * * * * * * //
// //
// - - - - - - - - - - - - - - - - - Geometry - - - - - - - - - - - - - - - //
// //
sc 0.001; // Scaling factor (sc = 0.001 ==> d = 1 mm) //
li 0.5; // Inlet length (in d) //
// list of z and y coordinates of nozzle contour //
#include "Meas_Cyl.out"; //
// //
// - - - - - - - - - - - - - - - - - - Mesh - - - - - - - - - - - - - - - - //
// //
cy 90; // Number of cells in y of nozzle //
cz 600; // Number of cells in z of nozzle //
gy 10; // Grading in y towards nozzle wall //
// //
// * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * * //
User input mask (in blockMeshDict)
2D meshing tool to create an arbitrary nozzle contour

## Slide 15: 2. Mesh creation
y
z
2D meshing tool to create an arbitrary nozzle contour
Use the following command to create the mesh
blockMesh && extrudeMesh &
Mesh is created 
/
/
The following folders have been created and contain mesh information
Command checkMesh can be used to check the mesh metrics (skewness, orthogonality, aspect ratio, etc.)
Let‘s see the mesh in ParaView

## Slide 16: Agenda (Part 1)
Geometry creation
Mesh creation
Numerical setup
  Boundary conditions
  Turbulence model
  Real gas model
  Numerical settings
/
/
/
turbulent thermal diffusivity
turbulence kinetic energy
turbulent viscosity
turbulence specific dissipation rate
pressure
temperature
velocity
thermophysical properties
turbulence properties
mesh settings
simulation settings
decomposition settings
mesh extrusion settings
numerical schemes
numerical solvers
nozzle contour file
OpenFOAM folder structure
Pre-processing

## Slide 17: 3.a) Boundary conditions
top
axis
front
back
inlet
outlet
First, let‘s estimate the throat Reynolds number

## Slide 18: 3.a) Boundary conditions
Throat Reynolds number
Ideal mass flow rate
Use definitions from ISO 9300
For reasons of simplicity, assume ideal gas and isentropic, 1D flow
We often take this expression for granted
But how can we actually derive this formulation?
Estimation of throat Reynolds number

## Slide 19: 3.a) Boundary conditions
Mass flow rate
Critical area
critical*
How can we derive this equation?
Start with simple definition:
Assume:
  Ideal gas
  Reversible process
  Adiabatic process
  1D flow
Isenthalpic process
(constant total enthalpy)
Critical Mach number
Critical temperature is still unknown
Ideal gas
Rearranging
Critical velocity

( in ISO 9300)

## Slide 20: 3.a) Boundary conditions
Mass flow rate
Critical area
critical*
How can we derive this equation?
Start with simple definition:
Critical velocity
Critical density
Isentropic process
(constant entropy)
Ideal gas law
With critical temperature


Assume:
  Ideal gas
  Reversible process
  Adiabatic process
  1D flow

## Slide 21: 3.a) Boundary conditions
Mass flow rate
Critical area
critical*
How can we derive this equation?
Start with simple definition:
Critical velocity
Critical density
Rearranging



Assume:
  Ideal gas
  Reversible process
  Adiabatic process
  1D flow
ISO 9300

## Slide 22: 3.a) Boundary conditions
Estimation of throat Reynolds number
Throat Reynolds number
Ideal mass flow rate
Ideal critical flow factor
Dynamic viscosity (REFPROP):
Universal gas constant:
Molar mass:
Let‘s set the boundary conditions in OpenFOAM

## Slide 23: 3.a) Boundary conditions
Pressure p
Mass [kg]
Length [m]
Time [s]
Temperature [K]
Quantity [mol]
Current [A]
Luminous intensity [cd]
= Pascal [kgm-1s-2]
= Initial distribution inside of the nozzle (200 bar)
= Actual boundary conditions for each patch face

## Slide 24: 3.a) Boundary conditions
Pressure p
Temperature T
Velocity U
Wall:
No-slip
Adiabatic
Inlet:
Total pressure
Total temperature
Outlet:
Static pressure
Axis:
Rotation axis
Front and Back:
Symmetry

## Slide 25: Agenda (Part 1)
Geometry creation
Mesh creation
Numerical setup
  Boundary conditions
  Turbulence model
  Real gas model
  Numerical settings
/
/
/
turbulent thermal diffusivity
turbulence kinetic energy
turbulent viscosity
turbulence specific dissipation rate
pressure
temperature
velocity
thermophysical properties
turbulence properties
mesh settings
simulation settings
decomposition settings
mesh extrusion settings
numerical schemes
numerical solvers
nozzle contour file
OpenFOAM folder structure
Pre-processing

## Slide 26: 3.b) Turbulence model
The turbulence model is selected in the turbulenceProperties file
Banana?
banana;
The ‚banana trick‘ provokes an error message to show all valid types
We select the RAS type
‚Banana trick‘ output

## Slide 27: 3.b) Turbulence model
Solved in additional transport equations
k-ω Shear Stress Transport (SST) model
Two-equation model for turbulent kinetic energy k and turbulent specific dissipation rate ω
Eddy viscosity model based on Boussinesq‘s hypothesis
Combines strenghts of k-ω model (inner region of boundary layer) and k-ε model (free stream)
The turbulence model is selected in the turbulenceProperties file
Reynolds-averaged simulation (RAS)
We solve for four additional quantities:
  Turbulent kinetic energy k
  Turbulent specific dissipation rate ω
  Turbulent viscosity νt
  Turbulent thermal diffusivity αt
Modeled and included in momentum equation
Modeled and included in energy equation

## Slide 28: 3.b) Turbulence model
How can we calculate the inlet value?
  For isentropic turbulence, kin can be estimated by:
  Estimated turbulence intensity:
  Free stream velocity (based on preliminary calculations):
Turb. kin. energy k
Chosen wall function for k
  Provides a wall constraint depending on the y+ value

## Slide 29: 3.b) Turbulence model
How can we calculate the inlet value?
  ωin is calculated as:
  Turbulence length scale (fully developed pipe flow):
  Inlet diameter:
  Model parameter:
Turb. kin. energy k
Turb. diss. rate omega
Chosen wall function for ω
  Provides a wall constraint depending on the y+ value

## Slide 30: 3.b) Turbulence model
Turb. kin. energy k
Turb. diss. rate omega
Turb. viscosity nut
Chosen wall function for νt
  Provides a wall constraint depending on the y+ value

## Slide 31: 3.b) Turbulence model
Turb. kin. energy k
Turb. diss. rate omega
Turb. therm. diff. alphat
Chosen wall function for αt
  Provides a wall constraint depending on the y+ value

## Slide 32: 3.b) Turbulence model
Turb. kin. energy k
Turb. diss. rate omega
Turb. viscosity nut
Turb. therm. diff. alphat

## Slide 33: Agenda (Part 1)
Geometry creation
Mesh creation
Numerical setup
  Boundary conditions
  Turbulence model
  Real gas model
  Numerical settings
/
/
/
turbulent thermal diffusivity
turbulence kinetic energy
turbulent viscosity
turbulence specific dissipation rate
pressure
temperature
velocity
thermophysical properties
turbulence properties
mesh settings
simulation settings
decomposition settings
mesh extrusion settings
numerical schemes
numerical solvers
nozzle contour file
OpenFOAM folder structure
Pre-processing

## Slide 34: 3.c) Real gas model
Critical temperature [K]
Critical volume [m3/kmol]
Critical pressure [Pa]
Molar mass [g/mol]
Developed
real gas model
The real gas model for hydrogen is selected in the thermophysicalProperties file
GitLab link
Real gas settings
r
Ideal gas settings
can be used for low pressure cases

## Slide 35: Agenda (Part 1)
Geometry creation
Mesh creation
Numerical setup
  Boundary conditions
  Turbulence model
  Real gas model
  Numerical settings
/
/
/
turbulent thermal diffusivity
turbulence kinetic energy
turbulent viscosity
turbulence specific dissipation rate
pressure
temperature
velocity
thermophysical properties
turbulence properties
mesh settings
simulation settings
decomposition settings
mesh extrusion settings
numerical schemes
numerical solvers
nozzle contour file
OpenFOAM folder structure
Pre-processing

## Slide 36: 3.d) Numerical settings
Compressible flow solver
Start and end time
Time step of the simulation
In the controlDict file, the main case controls are set (e. g. time and write settings, functions objects, etc.)
How can we estimate an appropriate magnitude for the time step Δt?
  Start with CFL condition in the axial direction at the nozzle throat:
Cell size in the axial direction
Velocity at nozzle throat
This value can be used as a starting point
Chosen time step (0.25·10-8 s) is smaller due to stability reasons

## Slide 37: 3.d) Numerical settings
Compressible flow solver
Start and end time
Time step of the simulation
Control to adjust time step during simulation (here: not active)
Adjusts time step to coincide with writeInterval (for automatic time stepping)
Controls number of stored time directories (set to 0 to disable this)
Specifies data file format and precision, and whether they are compressed or not
Format and precision of the naming of the time directories
Allows user to modify parameters during simulation
In the controlDict file, the main case controls are set (e. g. time and write settings, functions objects, etc.)

## Slide 38: 3.d) Numerical settings
Calculates mass flow rate at the inlet patch in every time step (deltaT) and stores it in a text file
Calculates Mach number distribution at defined time intervals (writeInterval) and stores it in the time directories
Calculates density distribution at defined time intervals (writeInterval) and stores it in the time directories
Note: this is a user-defined function and library (suiting our developed real gas model)
/
/
/
/
…
Functions objects are specified under functions (included in controlDict file)
Storage location

## Slide 39: 3.d) Numerical settings
Time schemes
Interpolation schemes
Surface-normal gradient schemes
Wall distance calculation method
Gradient schemes
Laplacian schemes
Divergence schemes
General:
phi: Flux across cell faces
Gauss: Gaussian integration
Time scheme:
Euler: First order, implicit, bounded
Discretization schemes:
linear: Second order, unbounded
limitedLinear: First / second order, unbounded
upwind: First order, bounded
Correction scheme:
corrected: Second order, non-orthogonality
First order: bounded / stable but diffusive
Second order: accurate but might oscillate
Compromise between accuracy and stability
In the fvSchemes file, the numerical schemes are set
Keywords:
Remember:

## Slide 40: 3.d) Numerical settings
PIMPLE algorithm
Pressure-velocity coupling algorithm fulfilling momentum and continuity equation in each time step
Diagonal solver for explicit systems
Symmetric Gauss-Seidel solver
nOuterCorrectors: number of momentum predictor (outer) loops
nCorrectors: number of velocity corrector (inner) loops
nNonOrthogonalCorrectors: number of pressure (inner) loops
In the fvSolution file, solvers, tolerances, and algorithms are set
nCorrectors
nNonOrthogonal
Correctors
nOuterCorrectors
Momentum
predictor
PIMPLE algorithm (simplified)
Pressure equation
Velocity corrector

## Slide 41: 3.d) Numerical settings
Parallel run:
Decompose flow domain into subdomains
decomposePar &
Start parallel simulation and write log file
mpirun -np 4 sonicFoam -parallel > log &
Reconstruct flow domain (after simulation)
reconstructPar &
Serial run:
Start simulation and write a log file
sonicFoam > log &
Simulation running
Run simulation
Let‘s have a coffee break until the simulation is completed
Option 1
Option 2
0
1
2
3
decomposeParDict

## Slide 42
Five-minute break

## Slide 43: Agenda (Part 2)
Log file
Convergence
  Residuals
  Mass flow rate
Discharge coefficient
Flow field
  Surface plots
  Line plots
/
/
Mach number
density
internal energy
turbulent kinetic energy
turbulent specific dissipation rate
pressure
radial velocity
axial velocity
inlet mass flow rate
/
/
/
Post-processing
OpenFOAM folder structure

## Slide 44: Agenda (Part 2)
Log file
Convergence
  Residuals
  Mass flow rate
Discharge coefficient
Flow field
  Surface plots
  Line plots
/
/
Mach number
density
internal energy
turbulent kinetic energy
turbulent specific dissipation rate
pressure
radial velocity
axial velocity
inlet mass flow rate
/
/
/
Post-processing
OpenFOAM folder structure

## Slide 45: 4. Log file
Let‘s have a look at the log file:
  Command: vim log
Time step
Run completed
Writing function objects
Courant number
1st PIMPLE outer loop
2nd PIMPLE outer loop
Run time

## Slide 46: Agenda (Part 2)
Log file
Convergence
  Residuals
  Mass flow rate
Discharge coefficient
Flow field
  Surface plots
  Line plots
/
/
Mach number
density
internal energy
turbulent kinetic energy
turbulent specific dissipation rate
pressure
radial velocity
axial velocity
inlet mass flow rate
/
/
/
Post-processing
OpenFOAM folder structure

## Slide 47: 5.a) Residuals
Let‘s check the convergence of the simulation
First, we extract the residual data from the log file:
  Command: foamLog log &
This generates a /logs folder
Let’s plot the residuals from the output data
Residuals quicky drop and slightly oscillate around a constant value

## Slide 48: Agenda (Part 2)
Log file
Convergence
  Residuals
  Mass flow rate
Discharge coefficient
Flow field
  Surface plots
  Line plots
/
/
Mach number
density
internal energy
turbulent kinetic energy
turbulent specific dissipation rate
pressure
radial velocity
axial velocity
inlet mass flow rate
/
/
/
Post-processing
OpenFOAM folder structure

## Slide 49: 5.b) Mass flow rate
Let‘s see how the mass flow rate is establishing
We monitored the mass flow rate at the inlet
< 0.015 %
Mass flow rate only varies within 0.015 % margin
Mean value

## Slide 50: Agenda (Part 2)
Log file
Convergence
  Residuals
  Mass flow rate
Discharge coefficient
Flow field
  Surface plots
  Line plots
/
/
Mach number
density
internal energy
turbulent kinetic energy
turbulent specific dissipation rate
pressure
radial velocity
axial velocity
inlet mass flow rate
/
/
/
Post-processing
OpenFOAM folder structure

## Slide 51: 6. Discharge coefficient
Let‘s calculate the discharge coefficient
Area of CFD domain
Ideal gas
Real gas
(From REFPROP)
Relation

## Slide 52: Agenda (Part 2)
Log file
Convergence
  Residuals
  Mass flow rate
Discharge coefficient
Flow field
  Surface plots
  Line plots
/
/
Mach number
density
internal energy
turbulent kinetic energy
turbulent specific dissipation rate
pressure
radial velocity
axial velocity
inlet mass flow rate
/
/
/
Post-processing
OpenFOAM folder structure

## Slide 53: 7.a) Surface plots
We introduced a specific function for the Mach number for our real gas model for hydrogen
Why is this necessary?
In OpenFOAM (OF), the Mach number function is defined as follows:
Here, the ideal isentropic exponent is used
For a real gas, the isentropic exponent is defined as follows:
Our Mach number function directly uses the speed of sound correlation areal:
Mach number function for real gas hydrogen
Let‘s see how to create surface plots like this

## Slide 54: 7.a) Surface plots
ParaView to visualize the flow field
Time step
Variable
3. Calculator
2. Contour
1. Surface
1. Surface plots
2. Contour plots
3. Calculated variables
Compressibility factor Z

## Slide 55: 7.a) Surface plots
Numerical Schlieren
Source: S. Matsuo et al., "Effects of Supersonic Nozzle Geometry on Characteristics of Shock Wave Structure“, Open Journal of Fluid Dynamics, Vol. 2 No. 4A, 2012.
Experimental Schlieren
(for qualitative comparison)
Gradient of Unstructured DataSet filter
Set density gradient
Apply X Ray colormap
Adjust Min. and Max. values

## Slide 56: Agenda (Part 2)
Log file
Convergence
  Residuals
  Mass flow rate
Discharge coefficient
Flow field
  Surface plots
  Line plots
/
/
Mach number
density
internal energy
turbulent kinetic energy
turbulent specific dissipation rate
pressure
radial velocity
axial velocity
inlet mass flow rate
/
/
/
Post-processing
OpenFOAM folder structure

## Slide 57: 7.b) Line plots
Plot velocity over nozzle throat height
Plot Over Line filter
Define the line location
Select the velocity
Save line data as text file

## Slide 58: Thank you!

## Slide 60
Sebastian Weiss
Working Group 8.41 “Modelling and Simulation” and Working Group 1.45 “Hydrogen Quantity Metering” Physikalisch-Technische Bundesanstalt (PTB) Berlin, Germany
sebastian.weiss@ptb.de